National Institute for Space Research (INPE) Emergency Request Form
Please be aware that you may receive additional ERFs for this activation. If you do receive a new ERF, it will be a request for additional data, not replacing the previous request

INPE Offer:

INPE is offering CBERS-4 and CBERS-4A satellite data to the Charter.

Hours of Service:

11:00-19:00 UTC

Procedure

• The INPE ERF and the General ERF shall be sent through COS-2 or, in case of system unavailability,  manually to: orderdesk@inpe.br

• Requests for new acquisition received before 15:00 UTC will be considered for a possible acquisition the following day.

• Archive data will be made available the same day.
Satellite(s) system characteristics and product description

| Satellite | Instruments | Modes | Resolution (m) | SWATH | WIDTH (along track) | FoV | Revisit (days) | Bands | # of satellites | Default product | #1 | #2 | #3 | Format |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| AMAZONIA-1 | WFI |  | 60 | 850 | 850 | Nadir | 5 | Multispectral: B1 450-520 nm B2 520-590 nm B3 630-690 nm B4 770-890 nm | 1 | L1D | L1A | L1B | L1D | GeoTIFF |
| CBERS-4 | MUX |  | 20 | 120 | 120 | Nadir | 26 | Multispectral: B5 450-520 nm B6 520-590 nm B7 630-690 nm B8 770-890 nm | 1 | L1D | L1A | L1B | L1D | GeoTIFF |
|  | PAN |  | 5 | 60 | 120 | Nadir to ±32° | 3 | Panchromatic: B1 510-730 nm Multispectral: B2 520-590 nm B3 630-690 nm B4 770-890 nm | 1 | L1D | L1A | L1B | L1D | GeoTIFF |
|  | WFI |  | 64 | 866 | 866 | Nadir | 3 | B5 450-520 nm B6 520-590 nm B7 630-690 nm B8 770-890 nm | 1 | L1D | L1A | L1B | L1D | GeoTIFF |
| CBERS-4A | MUX |  | 16 | 95 | 95 | Nadir to ±32° | 5 | Multispectral: B5 450-520 nm B6 520-590 nm B7 630-690 nm B8 770-890 nm | 1 | L1D | L1A | L1B | L1D | GeoTIFF |
|  | WFI |  | 55 | 685 | 685 | Nadir to ±32° | 5 | Multispectral: B13 450-520 nm B14 520-590 nm B15 630-690 nm B16 770-890 nm | 1 | L1D | L1A | L1B | L1D | GeoTIFF |
|  | WPM |  | 2 | 92 | 92 | Nadir to ±32° | 5 | Panchromatic: B0 450-900 nm Multispectral: B1 450-520 nm B2 520-590 nm B3 630-690 nm B4 770-890 nm | 1 | L1D | L1A | L1B | L1D | GeoTIFF |

INPE EMERGENCY REQUEST FORM (specific part)

Call ID: CallID

DATE/Time received at INPE: INPE On-Call:

INPE Internal Use Only Order ID #:

Planning Order:

☒   CBERS4 PAN (Res: 5m; swath: 60km; scene length: 120km)

## Area of Interest (download KML file with all areas including precise locations)

## ☒ ID 890-1 Dera Ghazi Khan priority 1 comment:

## Precise location precise-location-1:

## Lat: 30.051

## Long: 70.6824

## Radius(km): 26.0

## First Acquisition:

## ⃝    First Acquisition Date: yyyy/mm/dd

## 🔘 As Soon as Possible

## ☒ ID 890-3 Kashmore priority 1 comment:

## Precise location precise-location-1:

## Lat: 28.39

## Long: 69.6387

## Radius(km): 43.0

## First Acquisition:

## ⃝    First Acquisition Date: yyyy/mm/dd

## 🔘 As Soon as Possible

## ☒ ID 890-5 Mirpur Khs priority 1 comment:

## Precise location precise-location-1:

## Lat: 25.5186

## Long: 69.0051

## Radius(km): 23.0

## First Acquisition:

## ⃝    First Acquisition Date: yyyy/mm/dd

## 🔘 As Soon as Possible

☒   CBERS4A WPM (Res: 2m; swath: 92km; scene length: 92km)

## Area of Interest (download KML file with all areas including precise locations)

## ☒ ID 890-1 Dera Ghazi Khan priority 1 comment:

## Precise location precise-location-1:

## Lat: 30.0462

## Long: 70.6897

## Radius(km): 26.0

## First Acquisition:

## ⃝    First Acquisition Date: yyyy/mm/dd

## 🔘 As Soon as Possible

## ☒ ID 890-3 Kashmore priority 1 comment:

## Precise location precise-location-1:

## Lat: 28.3997

## Long: 69.646

## Radius(km): 45.0

## First Acquisition:

## ⃝    First Acquisition Date: yyyy/mm/dd

## 🔘 As Soon as Possible

## ☒ ID 890-5 Mirpur Khs priority 1 comment:

## Precise location precise-location-1:

## Lat: 25.5186

## Long: 69.0106

## Radius(km): 26.0

## First Acquisition:

## ⃝    First Acquisition Date: yyyy/mm/dd

## 🔘 As Soon as Possible

Archived Order:

☒   CBERS4

## Acquisition:

## 🔘 Most Recent

## ⃝    Same Season

☒   CBERS4A

## Acquisition:

## 🔘 Most Recent

## ⃝    Same Season

Additional Requests:

Approved by INPE: Date/Time: Comments:

INPE Internal Use Only