## Slide 1
Gilberto Camara, Max J. Egenhofer, Karine Ferreira, Pedro Andrade, Gilberto Queiroz, Alber Sanchez, Jim Jones, and Lubia Vinhas
image: INPE
Fields as a Generic Data Type for Big Spatial Data

## Slide 2
social networks
sensors everywhere
mobile devices
ubiquitous imagery
Earth observation and navigation satellites, mobile devices, social networks, and smart sensors: Big geospatial data.

## Slide 3
How can we best use the information provided by big data sources?
Big data requires new conceptual views
Image source: Geoscience Australia

## Slide 4: Layer-Based GIS: Few and different data sources Big Data GIS: Lots of similar data sources
Big data does not fit into the “map as set of layers” model
Image sources: GAO, Geoscience Australia

## Slide 5
An example of big geospatial data
image source: NOAA
ARGO buoys - 3,500 floats
120,000 temp, salinity, depth profiles/year

## Slide 6
ARGO buoys: innovative technology
Sensors measure down to 2,000 m, 10-Day Cycle
Floating buoys measuring properties of the oceans
images source: NOAA

## Slide 7: Another example: Free and big Earth Observation data
Image source: NASA
Open access data (US, EC, BR, CH): 5Tb/day

## Slide 8
Earth observation satellites provide key information about global change …
… but that information needs to be modeled and extracted

## Slide 9
To deal with big geospatial data, we need to reassess the core concepts of Geoinformatics

## Slide 10
Premise 1: Reality exists independently of human representations and changes continuously

## Slide 11
Premise 2: We have access to the world through our observations

## Slide 12: Premise 3: Computer representations of space and time should approximate the continuity of external reality

## Slide 13
Conjecture 1: Data models for space-time data should be as generic as possible
We need to represent volume, variety, velocity

## Slide 14
Conjecture 2: Space-time data models need observations as their building blocks
An observation is a measure of a property in space-time

## Slide 15
Conjecture 3. Sensors only provide samples of the external reality
To represent the continuity of world, we need more!
Willis Eschenbach

## Slide 16
temp = (2 + sin(2 π* (julianday + lag)/365.25)) ˆ1.4
Willis Eschenbach
Conjecture 4: Approximating external reality needs space-time data samples and estimators

## Slide 17: Conjecture 5: Fields = Sensor data + Estimators
A field estimates values of a property for all positions inside its extent
(fields simulate the continuity of external reality)

## Slide 18
Fields as a Generic Data Type
estimate: Position  Value
Positions at which estimations are made
Values that are estimated for each position

## Slide 19
Fields as a Generic Data Type
estimate: Position  Value
Positions are generic locations is space-time
Values are generic estimates for each position

## Slide 20
Fields as a Generic Data Type
estimate: Position  Value
Instances of Position: space, time, and space-time
Instances of Value: numbers, strings, space-time

## Slide 21
An Australian Geoscience Data Cube
A time series field (tsunami buoy)
positions: time values: wave height
image: Buoy near the coast of Japan

## Slide 22
An Australian Geoscience Data Cube
A coverage field (remote sensing image)
image: USGS
positions: 2Dspace values: soil reflectance

## Slide 23
An Australian Geoscience Data Cube
coverage set
images: USGS
A field of fields
positions: time values: coverages (2DSpace number)

## Slide 24
A trajectory field
positions: time values: space
 8/8/99
 11/7/03
Japan/East Sea
Russia
Japan
Argo float UW 230
deployed 02.08.1999
10-day interval data
until 07.11.2003
source: Stephen Riser
University of Washington

## Slide 25
A field of fields (Argo floats in Southern Ocean)
Positions: space Values: trajectories (time  space)

## Slide 26
A space-time field extracted from float data
Positions: space-time Values: water temperature

## Slide 27: Different choices for spatial estimators: same data source, different fields
Observations
of soil profiles
Geostatistics
Gravitational
Voronoi
Notes: Parte 1: definições, conceitos, os quatro universos de representação, modelagem de dados;
Parte 2: estrutura dual, bancos de dados relacionais, consulta espacial;
Parte 3: aspectos interdisciplinares, modelagem matemática, integração de dados, generalização;
Parte 4: principais operadores, álgebra de mapas, LEGAL, menus e formulários x linguagem de alto nível;
Parte 5: apresentação dos detalhes de alguns projetos tipicamente ambientais e cadastrais.

## Slide 28: Field data model
Field F [P:Position, V:Value, E:Extent, G:Estimator]
F1
domain(f1) = {p1,p2,p3}
estimate (f1, pnew) = g(f1, pnew)
extent (f1) = δ(A)
p1
p2
p3
pnew
Domain defines granularity
Estimator provides value on all positions inside the extent
extent
A

## Slide 29
External Reality
Observ.
Fields
Objects
Events
Conjecture 6: To identify objects and events in our descriptions of reality, we need first to define fields

## Slide 30: What is a geo-sensor?
What is a geo-sensor?
measure (s,t) = v
s ⋲ S - set of locations in space
t ⋲ T - is the set of times.
v ⋲ V - set of values
Field [E, P, V, G] uses E:Extent, P:Position, V:Value, G:Estimator
new: E x G → Field
add: Field x (P, V) → Field
obs: Field → {(P, V)}
domain: Field → {P}
extent: Field → E
estimate: Field x P → V
subfield: Field x E → Field
filter: Field x (V → Bool) → Field
map: Field x (V → V) → Field
combine: Field x Field x (V x V → V) → Field
reduce: Field x (V x V → V) → V
neigh: Field x P x (P x P → Bool) → Field

## Slide 31
How can we make the Fields model work in practice?
Image sources: INPE, Filip Biljecki, UNAVCO

## Slide 32: Scientific data: multidimensional arrays
X
y
t
g = f(<x,y,t> [a1, ….an])

## Slide 33: Array databases: all data from a sensor put together into a single array
Field operations on positions in space-time
X
y
t

## Slide 34: SciDB architecture: “Shared nothing”
Large data is broken into chunks
Distributed server process data in parallel
image: Paul Brown (Paradigm 4)

## Slide 35: Mapping the Fields data model to SciDB
What we have in SciDB
Array management
Array analysis (linear algebra)
Scalability, distributed proc
What we need
Spatial, temporal, spectral, and semantic reference systems
Operations in space-time data

## Slide 36
An experiment on reproducible science using the Fields data model and SciDB

## Slide 37
S R Saleska et al., Science 2007;318:612
Did Amazon forests green up during 2005 drought?
An experiment on reproducible science
Forest canopy “greenness” JAS 2005
Significantly greater than average “greeness” JAS 2000-2006
“Greeness” measured by EVI (enhanced vegetation index)
Notes: Spatial pattern of July to September 2005 standardized anomalies (3) in (A) precipitation (derived from Tropical Rainfall Measuring Mission satellite observations during 1998–2006) and in (B) forest canopy “greenness” (the EVI derived from MODIS satellite observations during 2000–2006). (C) Frequency distribution of EVI anomalies from intact forest areas in (B) that fall within the drought area [red areas in (A), see fig. S2], significantly (P < 0.001) (3) skewed toward greenness.

## Slide 38
Data: MODIS MOD9Q1 product
250 mts spatial resolution, 8 days temporal resolution
4800 x 4800 pixels, 3 bands (red, nir, qc)
13 years of data (since 2000)
image: NASA
Notes: 38

## Slide 39
4,000 MODIS tiles (92 billion cells), 7 field functions,
4.6 hours processing
Reproducing big data science with SciDB and the Field data model
Extract the subarray covering Amazonia (filter)
EVI for each cell in all time steps (map)
EVI mean and stdev for JAS 2000-2006 for each cell (filter + map)
EVI mean for JAS 2005 for each cell (filter + map)
Compare EVI mean (JAS 2005) to the JAS 2000-2006 mean (combine)

## Slide 40: Our goal for the Fields data model
Remote visualization and
method development
Big data EO management and analysis
40 years of Earth Observation data of land change accessible for analysis and modelling.
Field
operations

## Slide 41
Conclusion 1:
The Fields data type is a generic model for
different kinds of big space-time data
image: INPE

## Slide 42
Conclusion 2: The Fields data type enables a better description of
of big space-time data than the layer view
image: INPE

## Slide 43
Conclusion 3: The Fields data type may foster a new generation of GISs that deal with big space-time data
image: INPE